## Slide 1: Silicon Epitaxy by Molten Salt Electrolysis
Sarat Buasai, Alexander McMahon, Yi Jie Wu
Advisors: Adam C. Powell, N. Aaron Deskins, Walter Towner

## Slide 2: 01 Background Project Goal Methods 02 03 04 05 06 Results and Discussion Conclusion Acknowledgement

## Slide 3: Background

## Slide 4: Background
Davis et al., Science 360:1419 (2018)
Main Problem
Reduction of greenhouse gases emission
Reforming the Solar Silicon Production process

## Slide 5: State of Solar Silicon
Prices surged between 2005 and 2008
Predictions of increase in Solar Silicon Demand
  Jacobson Scenario: 100% Sustainable energy by 2050, 58% solar
  Bloomberg New Energy Finance: 48% Sustainable, 24% Solar
  Del Norske Veritas and Germanischer Lloyd: 50% Sustainable Energy, 17% Solar
Current silicon production capacity can only support the latter two

## Slide 6: Main Production Methods Siemens Process Silane Pyrolysis Metallurgical Pathways
Main Method
Produces 90% of Solar Silicon
Purest Product
Alternative
Near Similar to Siemens
Direct refinement of MG-Si to Solar Silicon
Most Sustainable

## Slide 7: Silicon Production
Molten Salt Electrolysis - Inert Anode
Electrorefining
Image source: Y. Delannoy, J. Cryst. Growth 360:61-67 (2012)

## Slide 8: Molten Salt Electrolysis (MSE)
The Process
  Combination of salts heated in a furnace
  Electric current passed through molten slurry from cathode to anode
  Deposition of metal experienced at the cathode
  Oxygen produced at anode
Benefits
  No CO2 emissions
  Ultra-pure product

## Slide 9: State of MSE Research
Chloride and/or fluoride baths
Various starting materials
  Low and high purity
0.4V - 2V systems
Current densities of 0.15-0.20A/cm2
Multiple purity levels obtained
Thin film and crystalline silicon products

## Slide 10: A Potential Solution
Bath Composition
  MgF2-CaF2-CaO2-YF3-SiO2
Starting Material
  High Purity Quartzite (SiO2)
Electrical Input
  100kA Cell
  4.5V
Product Purity
  0.1ppm Al
  0.02ppm B
Current Density
  0.47A/cm2 at the Anode
  0.25A/cm2 at the Cathode
Product Form
  Crystalline Si
  Cut from Cathode

## Slide 11: Research Question
Analyze the process of solar grade silicon production from MgF₂-CaF₂-YF₃-CaO-SiO₂ bath molten salt electrolysis by completing the mass and energy balances of the process, determining the technological feasibility by constructing a prototype cell using various programs and performing Finite Element Analysis, and ascertaining the economic feasibility by performing a cost analysis.

## Slide 12: Project Goals Goal 1 Goal 2
Determine the technological feasibility of manufacturing solar grade Silicon through Molten Salt Electrolysis
Ascertain the economical practicality of scaling up the process

## Slide 13: Methods

## Slide 14: Methods
Mass and Energy Balance
Axiomatic Design
CAD Cell Design
Finite Element Analysis
Cost Modeling

## Slide 15: Mass and Energy Balance Mass Balance Energy Balance
Development of PFD
Calculate the production rate
Rate of O2 dispersion
Calculate heat loss, dissociation potential, overpotential

## Slide 16: Cell Design and Modeling CAD Modeling Finite Element Analysis Axiomatic Design
Generation of potential electrolysis cell design, based on electronic needs of the system
Mesh development and analysis with software
Decomposition of cell design for ease of understanding

## Slide 17: Cost Modeling
Determine the financial viability of the plant
Consulted senior process potline engineer at Century Aluminum
Gained information on production, labour and construction

## Slide 18: Results and Discussion

## Slide 19: Energy Balance

## Slide 20: CAD Model - Preliminary 100kA Cell
100 kA Current Bus
20 slab cathodes
  1.4m x 0.7m x 0.02m
420 Cylindrical Anodes
  21x20 array
  0.03m radius
  52cm cylindrical height
Cell Footprint
  10.3m2
  Similar to existing Hall Heroult cells

## Slide 21: Preliminary Cell Modeling
Partial exploded view of electrodes
Slab cathode cell schematic
Switching setup
All cell renderings done in SolidWorks

## Slide 22: Theoretical Cell Modeling

## Slide 23: Cost Analysis: Cash Flow Diagram

## Slide 24: Cost Analysis
Silicon Price: $3.0 per kg Si
  Current Average Price: $14-15 per kg Si
Fixed Capital Investment: 2 Billion Dollars
Operating Cost: $1.6 per kg Si
Market Increase: 5% per year
Operating Cost Increase: 2% per year
Break Even Period: 11 Years

## Slide 25: Cost Analysis
Scale Up Analysis compared to Century Aluminum Production Plant
Energy Intensive: Can be Operated Solely on Renewable Energy
No CO2 Emission
Reduced the Silicon price by 55%

## Slide 26: Conclusion
Conclusion
  Energy-intensive
  Can be scaled up with a break even period of 11 years
    Cost of Silicon Product can be cut by 55%
  High annual operating cost, energy being the biggest factor
Future Work
  Thorough Experimentation
  More Variety in Molten Salt Cell Design
  Additional Modeling with Magneto Hydro Dynamics

## Slide 27: Acknowledgements
Adam C. Powell
Associate Professor, Mechanical Engineering, WPI
Walter Towner
Associate Teaching Professor, Industrial Engineering, WPI
N. Aaron Deskins
Associate Professor, Chemical Engineering, WPI
Uday Pal and his Research Group
Professor, Mechanical Engineering, Boston University
Christopher Ritter
Senior Process Potline Engineer, Century Aluminum
Aditya Moudgal
PHD Student, Mechanical Engineering, WPI
Mohammad Asadikiya
Post Doc Student, Mechanical Engineering, WPI

## Slide 28: References
Teixeira, L. A. V., & Morita, K. (2009). Removal of Boron from Molten Silicon Using CaO–SiO2 Based Slags. ISIJ International, 49(6), 783–787. doi: 10.2355/isijinternational.49.783
Woditsch, P., & Koch, W. (2002). Solar grade silicon feedstock supply for PV industry. Solar Energy Materials and Solar Cells, 72(1-4), 11–26. doi: 10.1016/s0927-0248(01)00146-5
Bye, G., & Ceccaroli, B. (2014). Solar grade silicon: Technology status and industrial trends. Solar Energy Materials and Solar Cells, 130, 634–646. doi: 10.1016/j.solmat.2014.06.019
J. Guo, T. Villalon, U. Pal, S. Basu, “Effect of Optical Basicity on the Stability of Yttria‐stabilized Zirconia in Contact with Molten Oxy‐fluoride Flux”, J. Am. Ceram. Soc. 101:3605-3616, 2018, DOI: 10.1111/jace.15496
U.S. Department of Energy. (2010). 2008 Solar Technologies Market Report. Energy Efficiency & Renewable Energy.
Jacobson MZ et al (2017) Joule 1:108. https://doi.org/10.1016/j.joule.2017.07.005
Powell, A. C. (2019). Recycling in Supply Chains for Tomorrow’s Low-Carbon Industries. REWAS 2019 The Minerals, Metals & Materials Series, 9–18. doi: 10.1007/978-3-030-10386-6_2
Polysilicon Shortage: Production Solar panels in Danger https://www.betterworldsolutions.eu/rawmaterial-shortage-production-solar-panels-danger/ (accessed Apr 27, 2020)
Yang, X., Ji, L., Zou, X., Lim, T., Zhao, J., Yu, E. T., & Bard, A. J. (2017). Toward Cost-Effective Manufacturing of Silicon Solar Cells: Electrodeposition of High-Quality Si Films in a CaCl2-based Molten Salt. Angewandte Chemie, 129(47), 15274–15278. doi: 10.1002/ange.201707635
Filtvedt, W. O., Holt, A., Javidi, M., Melaaen, M. C., Marstein, E., Ramachandran, P. A., & Tathgar, H. (2010). Development of fluidized bed reactors for silicon production. Solar Energy Materials and Solar Cells, 94(12), 1980–1995. doi: https://doi.org/10.1016/j.solmat.2010.07.027
Ramos, A., Filtvedt, W., Lindholm, D., Ramachandran, P., Rodríguez, A., & Cañizo, C. D. (2015). Deposition reactors for solar grade silicon: A comparative thermal analysis of a Siemens reactor and a fluidized bed reactor. Journal of Crystal Growth, 431, 1–9. doi: 10.1016/j.jcrysgro.2015.08.023
Osborne, M. (2014, January 9). Explosion at Mitsubishi polysilicon plant in Japan causes deaths. PVTECH. Retrieved from https://www.pv-tech.org/news/explosion_at_mitsubishi_polysilicon_plant_in_japan_causes_deaths

## Slide 29: References
Safarian, J., Tranell, G., & Tangstad, M. (2012). Processes for Upgrading Metallurgical Grade Silicon to Solar Grade Silicon. Energy Procedia, 20, 88–97. doi: 10.1016/j.egypro.2012.03.011
Morita, K., & Miki, T. (2003). Thermodynamics of solar-grade-silicon refining. Intermetallics, 11(11-12), 1111–1117. doi: 10.1016/s0966-9795(03)00148-1
Li, Y., Wu, J., Ma, W., & Yang, B. (2014). Boron Removal from Metallurgical Grade Silicon using a Refining Technique of Calcium Silicate Molten Slag Containing Potassium Carbonate. Silicon, 7(3), 247–252. doi: 10.1007/s12633-014-9222-2
de Wild-Scholten, M. J., Glockner, R., Odden, J. O., Halvorsen, G., & Tronstad, R. (2008). LCA Comparison of the Elkem Solar Metallurgical Route and Conventional Gas Routes to Solar Silicon.
Silicor Materials: Solar Silicon Manufacturer, San Jose, CA. (n.d.). Retrieved October 8, 2019, from https://www.silicormaterials.com/.
Nichol, S. (2010) United States Patent No. US 007727503B2
Haarberg, G. M. (2015). ELECTROCHEMICAL DEPOSITION OF HIGH PURITY SILICON FROM MOLTEN SALTS. Mediterranean Materials Congress on Energy and Infracstructure.
Dong, Y., Slade, T., Stolt, M. J., Li, L., Girard, S. N., Mai, L., & Jin, S. (2017). Low-Temperature Molten-Salt Production of Silicon Nanowires by the Electrochemical Reduction of CaSiO3. Angewandte Chemie, 129(46), 14645–14649. doi: 10.1002/ange.201707064
Haarberg, G. M., Kato, T., Norikawa, Y., & Nohira, T. (2019). Electrodeposition of Silicon with a Liquid Gallium Cathode in Molten Salts. ECS Transactions, 89(7), 29–35. doi: 10.1149/08907.0029ecst
Ramírez-Márquez, C., Otero, M. V., Vázquez-Castillo, J. A., Martín, M., & Segovia-Hernández, J. G. (2018). Process design and intensification for the production of solar grade silicon. Journal of Cleaner Production, 170, 1579–1593. doi: 10.1016/j.jclepro.2017.09.126
Glockner, R., & de Wild-Scholten, M. (2012). ENERGY PAYBACK TIME AND CARBON FOOTPRINT OF ELKEM SOLAR SILICON.
U.S. Department of Energy. (2010). 2008 Solar Technologies Market Report. Energy Efficiency & Renewable Energy.
Norgate, T., Jahanshahi, S., & Rankin, W. (2007). Assessing the environmental impact of metal production processes. Journal of Cleaner Production, 15(8-9), 838–848. doi: 10.1016/j.jclepro.2006.06.018
Yadav, S.; Chattopadhyay, K.; Singh, C. V. Solar Grade Silicon Production: A Review of Kinetic, Thermodynamic and Fluid Dynamics Based Continuum Scale Modeling. Renewable and Sustainable Energy Reviews 2017, 78, 1288–1314. https://doi.org/10.1016/j.rser.2017.05.019.